## Slide 1: ISS Lamp
Aka. Oooh.. I want one of those!

## Slide 2: Overview (original)
PC
-linux
-python
Heavens-above.com
-RGB LED’s (PWM)
USB

## Slide 3: Initial idea
Arduino +ethernet shield with POE
-fully embedded solution
-one connection (CAT5e w/POE)
-Display for info
-LED’s
-Maybe use the nabduino? (MPLABX)
uhaapi.com -> json
dk.pool.ntp.org –> time
NO-GO:
Only visible passes from uhaapi 
Not enough memory to parse HTML tables from heavens-above.com

## Slide 4: Revised idea
Arduino +ethernet shield with POE
dk.pool.ntp.org
Robottobox
-Python
Heavens-above.com
-ALL PASSES

## Slide 5: The arduino side of things aka. C++ and shitty sandboxes
Arduino abstraction layer pros/cons:
No interrupts
No direct timer access
PWM = analogWrite() … urgh.
Realtime, not so much.
HUGE userbase with good advice
Tons of ”ready to use” libraries

## Slide 6: Wat do?
Get NTP time
Get data about next pass
Calculate time to next pass
Display pass info on VFD
Pretend to be a clock (with 30 second NTP refresh)
At 5 minutes before pass, start countdown, flash lights
At pass start, light up. If pass is visible: Tell user where to look
At pass end, turn lights down.
Rinse, Repeat.

## Slide 7: ARDUINO CODE

## Slide 8: The robottobox side of things aka. Learning python
Open port 1337 (UDP)
listen for incoming message
Get heavens-above passes pages, both visible and non visible.
Visible passes ∊ All passes – so check for match, visible have priority
Remove passes that are in the past
Respond to sender with next pass data

## Slide 9: Parsed ISS data anatomy
  Regular pass example:
  “R 1354485026 S-10 1354485108 SE-12 1354485190 ESE-10”
  Visible pass example:
  “V -2.0 1354481759 SE-10 1354481769 S-22 1354481779 SW-10”
Regular
Start
Max
End
Visible
Magnitude

## Slide 10: Python CODE

## Slide 11: DEMO

## Slide 12: Future ideas:
Arduino +ethernet shield with POE
pool.ntp.org
Heavens-above.com
-ALL PASSES
-Parse pass data in memory friendly nibbles
Geolocation based on IP?
http://www.hostip.info/